## Slide 1
Electrical Engineering

## Slide 2
01
Introduction
The Problem
Human emotions are complex & subjective
Traditional methods rely on facial expressions or self-reports
These are easily faked or inaccurate
EEG brain signals cannot be masked — they are direct neural measurements
Real-time emotion recognition is critical for mental health, education & HCI
Our Solution
Use SEED EEG dataset (62-channel, 3-class emotions)
Extract de_LDS features — 310 features per second
Apply PCA to reduce noise and dimensionality
Train an SVM classifier with balanced class weights
Map emotion states to personalized study recommendations
EEG-Based Emotion Classification | SEED Dataset & SVM

## Slide 4
03
System Architecture
Step 1
EEG Data
(SEED Dataset)
62 Channels
15 Subjects
▶
Step 2
Feature
Extraction
de_LDS
310 Features/sec
▶
Step 3
PCA
Reduction
95% Variance
Noise Filtered
▶
Step 4
SVM
Classifier
Balanced Weights
RBF/Linear Kernel
▶
Step 5
Emotion
Prediction
Positive/Neutral
/Negative
Recommendation Engine
Emotion → Personalized Study Action
(Deep Work tasks, Pomodoro sessions, focus strategies)
Emotion output feeds adaptive recommendation
EEG-Based Emotion Classification | SEED Dataset & SVM

## Slide 5
04
Dataset & Feature Engineering
SEED Dataset
62
EEG Channels
15
Subjects
3
Sessions Each
30546
Total Samples
310
Features/second
Feature Engineering
de_LDS Features
Differential Entropy smoothed by Linear Dynamic System (LDS) — captures temporal dynamics of EEG brain activity across 5 frequency bands.
Second-by-Second
Data processed every 1 second rather than averaged over whole trials — captures micro-fluctuations in emotional states.
PCA (95% variance)
Principal Component Analysis reduces dimensionality, removes noise and collinear features, speeds up SVM training.
Class Balancing
SVM trained with balanced class weights to handle unequal class distribution in the SEED dataset fairly.
EEG-Based Emotion Classification | SEED Dataset & SVM

## Slide 6
05
SVM Classifier & Training
Why SVM for EEG?
Support Vector Machines find the optimal hyperplane to maximize the margin between classes. We specifically utilized an RBF (Radial Basis Function) Kernel, which excels at handling the highly non-linear separability inherent in human brainwaves.
1
Hyperparameter Tuning
Implemented an RBF Kernel with a regularization parameter (C =10) to strictly penalize misclassifications, and gamma = “scale” to adapt to the variance of the EEG features.
2
Class Weight Balancing
Applied class weight equals balanced within the SVM architecture. This mathematically penalizes the model for over-predicting the majority class, forcing it to learn the distinct borders of Negative, Neutral, and Positive states equally.
3
State Smoothing Logic
Real-time SVM predictions are volatile. We built a custom algorithm to calculate the modal prediction over a rolling 300-sample time window, converting erratic second-by-second guesses into a stable, dominant cognitive state.
EEG-Based Emotion Classification | SEED Dataset & SVM

## Slide 7
06
Recommendation Engine
😊 Positive
Focus is HIGH
Recommended Actions:
→ Complex Problem Solving / Math Sets (Deep Work)
→ Pomodoro Study Session (50/10) (Deep Work)
→ Learn New Concepts or Chapters
😐 Neutral
Focus is MODERATE
Recommended Actions:
→ Review Notes / Flashcards (Spaced Repetition)
→ Light Reading / Summarizing
→ Practice Problems (Medium Difficulty)
😔 Negative
Focus is LOW
Recommended Actions:
→ Take a Short Break (5-10 mins)
→ Mindfulness / Deep Breathing Exercise
→ Watch Educational Video (Passive Learning)
EEG-Based Emotion Classification | SEED Dataset & SVM

## Slide 8
07
Results — Classification Metrics
Overall Accuracy
65.17%
Samples: 30,546 | Balanced SVM | PCA (95% variance)
Class | Precision | Recall | F1-Score | Support
😔 Negative | 0.59 | 0.55 | 0.57 | 10,080
😐 Neutral | 0.56 | 0.69 | 0.62 | 9,936
😊 Positive | 0.84 | 0.72 | 0.78 | 10,530
Macro Avg | 0.66 | 0.65 | 0.65 | 30,546
💡 Positive emotion shows highest precision (0.84) — model is most reliable when user is engaged and happy
EEG-Based Emotion Classification | SEED Dataset & SVM

## Slide 9
08
Results — Confusion Matrix
Key Observations
7,574
Positive correctly classified (highest)
6,835
Neutral correctly classified
5,499
Negative correctly classified
4,180
Negative → Neutral confusion
EEG-Based Emotion Classification | SEED Dataset & SVM

## Slide 10
09
Results — Performance Chart
Chart: 
| Negative | Neutral | Positive
Precision | 0.59 | 0.56 | 0.84
Recall | 0.55 | 0.69 | 0.72
F1-Score | 0.57 | 0.62 | 0.78
Performance Summary
Overall Accuracy
65.17%
Macro Avg Precision
0.66
Macro Avg Recall
0.65
Macro Avg F1
0.65
Best Class
Positive
Hardest Class
Negative
EEG-Based Emotion Classification | SEED Dataset & SVM

## Slide 11
Thank You!
EEG-Based Emotion Classification using SEED Dataset & SVM
65.17%
Accuracy
de_LDS
EEG Features
SVM
Classifier
PCA 95%
Variance Kept
3-Class
Emotion States
🔗 github.com/Sumer7568/seed-emotion-classification
SEED Dataset | SVM Classification | Adaptive Recommendations